## Slide 1: NLRI Error handling draft-decraene-idr-nlri-error-handling-00
Bruno Decraene (Orange)
John G. Scudder (HPE)

## Slide 2: BGP error handling as per RFC 7606
Error-handling approaches:
Attribute discard (if no impact on routing)
Treat-as-withdraw (if all NLRI can be read)
Session reset (otherwise / if one NLRI can’t be parsed)
 Parsing all NLRIs is critical to avoid session reset

## Slide 3: NLRI with non-key data
Some AFI/SAFI encodes NLRI with both
Key (“prefix”)
Non-key data (kind of per NLRI attribute)
Examples of non-key data encoded in NLRI:
  Labeled Unicast: MPLS label stack
    Including BGP CT, IP VPN
  EVPN: MPLS label(s), (Ethernet Segment Identifier)
  BGP CAR: TLVs
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| NLRI Length | Key Length | NLRI Type | //
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ //
| Type-specific Key Fields //
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Non-Key TLVs Fields //
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 4: Error handling with non-key data
Non-key data in NLRI increases:
length of data to parse
parsing complexity (multiple fields, TLVs, MPLS end of stack bit…)
 chance of MP_REACH_NLRI parsing error
 BGP session reset (high network impact, not likely recoverable)

## Slide 5: Proposal (1)
New non-transitive BGP attribute: “NLRI_KEY_LIST”
  Same format as MP_UNREACH_NLRI (aka withdraw)
  Encoded first in the UPDATE, followed by MP_REACH_NLRI
If error condition in MP_REACH_NLRI preventing NLRI parsing
  Perform “Treat-As-Withdraw”, using the “withdraw” in the NLRI_KEY_LIST attribute
  Hence avoiding BGP session reset

## Slide 6: Proposal (2)
Straightforward
  (+) Reuse existing MP_UNREACH_NLRI format
    (+) Sender constructs NLRI_KEY_LIST as a regular MP_UNREACH_NLRI
    (+) Receiver reads NLRI_KEY_LIST as a regular withdraw/MP_UNREACH_NLRI
  (-) Extra complexity on the sender (encodes twice the NLRI list)
Optional.
Cost is supported by the AFI adding the non-key data complexity

## Slide 7: Use case example: BGP Label Unicast
PE1
RR1
RR2
PE1
PE2
PE3
PE4
PE1 originates a BGP LU route
  With a label stack of 2 MPLS labels
MP_REACH_NLRI encoding
  AFI: 1
  SAFI: 4
  Length of Next-Hop: 4
  Next-Hop: 1.0.0.1
  Reserved: 0
  Length: 80 bits
  Label1: 42
  Bottom of stack1: 0
  Label2: 52
  Bottom of stack2: 1
  Prefix: 1.0.0.1
A different color indicates a different implementation

## Slide 8: Current BGP error handling (w/ RFC 7606)
PE1
RR1
RR2
PE1
PE2
PE3
PE4
Red implementation does not understand the label stack
  Wrongly assumes a single label
PE1 originates and RR1, RR2 propagate the route
  Route is 100% correct as per RFC 3107
PE2…PE4
  can’t parse the NLRI in MP_REACH_NLRI
  can’t locate IP prefix (key)
   can’t treat as withdraw
  session reset
RR redundancy does not help
  RR code diversity does not help
A different color indicates a different implementation

## Slide 9: New proposal
PE1
RR1
RR2
PE1
PE2
PE3
PE4
BGP UPDATE message
NLRI_KEY_LIST
  AFI: 1
  SAFI: 4
  Length: 56 bits
  Compatibility field: 0x800000
  Prefix: 1.0.0.1
MP_REACH_NLRI
  AFI: 1
  SAFI: 4
  Length of Next-Hop: 4
  Next-Hop: 1.0.0.1
  Reserved: 0
  Length: 80 bits
  Label1: 42
  Bottom of stack1: 0
  Label2: 52
  Bottom of stack2: 1
  Prefix: 1.0.0.1
PE2…PE4
can’t parse the NLRI in MP_REACH_NLRI
can’t locate IP prefix (key)
Error handling: reads NLRI_KEY_LIST as a MP_UNREACH_NLRI
Effectively “Treat-as-withdraw”
No session reset
Builds on MP_UNREACH_NLRI being simpler than MP_REACH_NLRI
  Shorter in size, Fixed size, less fields
  no non-key data